## Slide 1: Hydrogen blend target analysis
Progress update
28 March 2019

## Slide 2: Hydrogen blending into gas distribution networks
Setting a hydrogen blending target
Propose a national hydrogen blending target (by volume), commencing at 0.15% from 2020 to 10% by 2030
Current national gas consumption of 387 PJ from customers connected to gas distribution networks (or 107 TWh). Excludes gas consumption by large industrial customers connected to gas transmission
387 PJ of gas consumption equates to 107 TWh of electricity consumption. Total NEM consumption of 180 TWh, including large industrial customers (Smelters)
To fully decarbonise 387 PJ of gas via electrolysis and renewable electricity, 40 GW of additional renewable generation capacity required
Calculated the electrolysis capacity required to meet blending targets. From 2 MW in 2020, ramping up slowly and accelerating from 2025 onwards – to take advantage of projected cost reduction in electrolysis (data sourced from manufactures, CSIRO and Morgan Stanley analysis); solar and wind generation costs (AEMO, ISP 2018)
Summary results
Total maximum retail price impact less than 0.7%
The cost of hydrogen production via electrolysis reduces from $60 per GJ (significant cost penalty as small scale demonstration projects) to about $12 per GJ, as projects are scaled up to meet targets
920 MW of electrolysis capacity built – provides sufficient scale platform to deliver further investment to meet exports

## Slide 3
10% blending target by volume (386 PJ, national gas consumption from distribution networks).
Hydrogen cost competitive by 2030. Maximum average price impact less than 0.7%
Chart: Blending target
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Electrolysis capacity required MW | 2.4364 | 3.776 | 23.0689 | 61.6627 | 149.0828 | 289.9905 | 480.1687 | 568.6999 | 754.2541 | 838.3683 | 920.8015
Hydrogen blending target (by volume) % | 0.00018 | 0.0003 | 0.002 | 0.006 | 0.015 | 0.03 | 0.05 | 0.06 | 0.08 | 0.09 | 0.1
Chart: $/GJ
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Cost of hydrogen production $/GJ | 60.5735 | 42.2269 | 32.7367 | 25.798 | 23.1592 | 20.1727 | 17.6602 | 15.304 | 13.9811 | 13.084 | 12.7538
Market price of natural gas $/GJ | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12
Total retail price impact % | 0.00010697 | 0.00015096 | 0.00058217 | 0.0012587 | 0.0025011 | 0.0040389 | 0.0054848 | 0.005888 | 0.00638 | 0.0064777 | 0.006528